02		DEPARTMENT OF PROFESSIONAL AND FINANCIAL REGULATION

174		BOARD OF BOILERS AND PRESSURE VESSELS

# Chapter 1:	DEFINITIONS

Summary: This Chapter defines (1) terms that are used in the rules adopted by the Board and (2) terms used in Title 32, Chapter 131, but not defined by statute. Terms used in the Board’s rules also are defined by statute and by the national codes adopted in Chapter 11.

# 1.	Incorporation by Reference; Conflicts

The Board incorporates in its rules the definitions that appear in 32 M.R.S.A. Chapter 131 and the national codes adopted in Chapter 11 of these Rules.

If a conflict exists as to definitions contained in any of the above sources, the definitions in Title 32, Chapter 131 prevail over both the definitions in the Board’s rules and the definitions in the national codes, and the definitions in the Board’s rules prevail over the definitions in the national codes.

# 2.	Definitions

As used in the Board’s rules, unless the context otherwise indicates, the following terms have the following meanings:

A.	ANSI. “ANSI” means the American National Standards Institute.

B.	ASME. “ASME” means the American Society of Mechanical Engineers International.

C.	Boiler. “Boiler” includes power boilers and low pressure boilers and means a closed vessel in which water is heated, steam is generated, steam is superheated, or any combination thereof, under pressure or vacuum for use external to itself by the direct application of heat. “Boiler” also includes fired units for heating or vaporizing liquids other than water where these units are separate from processing systems and complete within themselves. As used in the Board’s rules, the “boiler” includes only those units that are not exempt under 32 M.R.S.A. § 15102(1). When referring to power boilers, “boilers” includes boiler external piping.

D.	Boiler Operation. The Board recognizes 2 methods by which boilers are operated, manual and automatic.

(1)	“Manual operation” means that a full-time boiler operator or stationary steam engineer is required to observe boiler pressures, temperatures, and levels and to make adjustments as the output demand fluctuates. A partially automated boiler must be classified as being manually operated.

(2)	“Automatic operation” means that a boiler is fully equipped with automatic control systems and does not require a boiler operator or stationary steam engineer to make adjustments as the output demand fluctuates.

E.	Boiler Operator. “Boiler operator” means a licensed person who controls a low pressure boiler by observation and manipulation of mechanical, automatic, or remote control.

F.	Chief Inspector. “Chief Inspector” means the Chief Inspector of Boilers and Pressure Vessels or the Chief Inspector’s designee.

G.	Electric Boiler. “Electric boiler” means a power boiler or low pressure boiler in which the source of heat is electricity.

H.	Engineer-in-Charge. “Engineer-in-charge” means the licensed person designated by an owner to be responsible for ensuring that a boiler plant is maintained and operated in a safe condition by the company or organization to which the boiler or boilers are registered by the State of Maine.

I.	Low Pressure Boiler. “Low pressure boiler” means a boiler in which either: (1) steam or other vapor is generated at a pressure of no more than 15 PSIG or (2) fluid is heated to no more than 250 degrees Fahrenheit or the operating pressure is no more than 160 PSIG. “Low pressure boiler” is referred to as a “heating boiler” or a “process boiler.”

NOTE: Low pressure boiler types are identified in Section E-100 of Appendix E of Section IV of the ASME Boiler and Pressure Vessel Code.

J.	Inspector. “Inspector” means the Chief Inspector of Boilers and Pressure Vessels, a Deputy Inspector, or an Authorized Inspector, all as defined in 32 M.R.S.A. §15101.

K.	MAWP. “MAWP” means maximum allowable working pressure.

L.	National Board. “National Board” means the National Board of Boiler and Pressure Vessel Inspectors.

M.	NBIC. “NBIC” means the National Board Inspection Code.

N.	NPS. “NPS” means nominal pipe size.

O.	Organic Fluid Boiler. “Organic fluid boiler” means a pressure vessel in which organic fluid is vaporized or heated.

P.	Owner. "Owner" means a firm, person, partnership, association, corporation, or state or political subdivision that owns a boiler or pressure vessel.

Q.	Place Out of Service. “Place out of service” means to render safe and completely inoperable, other than to make repairs, for an indefinite period.

R.	Plant. “Plant” means the buildings, equipment, and fixtures of an institution or an industrial or manufacturing establishment at any one site.

(1)	Heating Plant. A “heating plant” consists of the boiler or boilers and the auxiliary equipment and would not necessarily include piping and radiation equipment used for space heating.

(2)	Power Plant. A “power plant” consists of the boiler or boilers, the auxiliary equipment and prime mover machinery used to produce electric power to be used outside the boiler and engine spaces.

(3).	Process Plant. A “process plant” consists of the boiler and the auxiliary equipment, which may or may not have prime moving machinery and will not necessarily include machinery and equipment used for manufacturing of a product. Process plant includes both low pressure and power boilers.

S.	Power Boiler. “Power boiler,” also commonly known as a “high pressure boiler,” means a boiler in which steam or other vapor is generated at a pressure of more than 15 PSI for use external to itself, and includes electric boilers, miniature boilers, organic fluid boilers, and high-temperature water boilers.

Note: The term “power boiler” includes boiler external piping up to and including the required stop valve(s).

T.	Pressure Vessel. “Pressure vessel” means a container for the containment of pressure, either internal or external. This pressure may be obtained from an external source, or by the application of heat from a direct or indirect source, chemical reaction, or any combination thereof. As used in the Board’s rules, “pressure vessel” includes only those units that are not exempt under 32 M.R.S.A. § 15102(2).

U.	PSI. “PSI” means pounds per square inch.

V.	PSIG. “PSIG” means pounds per square inch gauge.

W.	Relocation. “Relocation,” when applied to a boiler or pressure vessel, means movement of the boiler or pressure vessel to any extent from its current site. A “relocated” boiler or pressure vessel is a boiler, other than a portable boiler, or a pressure vessel that is moved.

X.	Reportable Accident. “Reportable Accident” means an unexpected and sudden event that renders a boiler or pressure vessel inoperative and adversely affects its pressure retaining capability.

Y.	Stamp. “Stamp” means a code symbol issued by the American Society of Mechanical Engineers or the National Board of Boiler and Pressure Vessel Inspectors. “Stamped” and “stamping” mean the application of such a code symbol.

Z.	Stationary Steam Engineer. “Stationary steam engineer” means a person licensed by the Board to operate a high pressure boiler or to be responsible for the operation and maintenance of equipment in a plant, in accordance with Maine law, and includes high pressure boiler operators.

AA.	Suspend Operation. “Suspend Operation” means the discontinuance of operation of a boiler or pressure vessel for any purpose, other than to make repairs, for a limited period of time.

AB.	TAPPI. “TAPPI” means Technical Association Pulp and Paper Industry.

# AUTHORITY: 	32 MRSA § 15101, § 15104-A, and § 15109

EFFECTIVE DATE:

January 15, 2005 – filing 2005-7