## Slide 1: PFAS Primer and a Simplified Groundwater Pathway CSM
Chris Evans
Senior Environmental Hydrogeologist
Maine DEP, Bureau of Remediation and Waste Management

## Slide 2: PFAS Primer
PFAS - Per- and Polyfluoroalkyl Substances
Class of Compounds – at least 3,000
All Anthropogenic – no naturally occurring PFAS
Suthersan et al. 2016

## Slide 3: PFAS Primer

## Slide 4: PFAS Primer
Stable, C-F bond strength Low volatility High molecular weight
Figure by D. Adamson, 2021, used with permission

## Slide 5: PFAS Primer
Better Living Through Chemistry
Oil and water resistant
Thermal and chemical stability (forever chemicals..)
Stain resistant
Friction reduction

## Slide 6: PFAS Primer
Environmental Release Sources
Fire Suppression and Training (AFFF)
Commercial - Industrial
Secondary Sources Like Biosolids/Sludge,
Landfills, Leachate

## Slide 7: PFAS Primer
Figure by L. Trozzolo, 2020 Used with permission

## Slide 8: Why Are We looking Now?
2009 Provisional Advisories : PFOS 200 ng/L (ppt),
PFOA 400 ng/L (ppt)
2013 USEPA UCMR3 testing of public water supplies >10,000 customers
2016 Updated and Final: Issued Lifetime Drinking Water Health Advisory PFOS + PFOA = 70 ng/L (ppt)
2018 Chapter 418 Criteria For Land Applied Residuals:
PFOA = .0025 mg/kg (2.5 ppb)
PFOS = .0052 mg/kg (5.2 ppb)
PFBS = 1.9 mg/kg (1900 ppb)
2021 LD129 Establishes an Interim Drinking Water Standard of 20 ppt for the Sum of 6 PFAS in Maine for Public water Supplies: PFOA, PFOS, PFDA, PFNA, PFHxS and PFHpA
Notes: An emerging contaminant is a chemical of concern which presents unique issues and challenges in the environment, but one which does not yet have enough exposure or health data to meet MCL criteria. Timing of DW HA coinciding with increasing awareness of extent in ME, initially from USAF/Navy evaluations, DoD leading without regulatory critieria in part due to large PWS impacts in other states (Pease in NH, Willow Grove in PA others)
March 2019 Governor’s PFAS Task Force announcement; - no action yet
With no MCL not technically a hazardous substance, DEP focus on DW supplies initially as priority, Chap 418 values due to concern with landspread near PWS
Details of development of HA and leaching values beyond this talk time
Why different than other HA – Lifetime and development effects and an immediate do not drink order if above conc threshold which is extremely small. Developmental effects are so sensitive that a single exposure at a critical time in development may produce an adverse outcome and these effects can impact a person over a lifetime.
Because they are persistent even short-term exposure can result in a body burden that persists for years. (if need for question response)
END
Challenging for State’s because was No draft review period before announcement of 2016 final, changed indiv PFOS and PFOA thresholds to a lower concentration AND combined them.
Lifetime HA defined by EPA OW as the concentration in DW that is not expected to cause any adverse noncarcinogenic effects for a lifetime of exposure;
In contrast the 10(-4) Cancer Risk level is the concentration of the contaminant in DW associated with a specific probability of cancer.
10(-4) Cancer Risk = conc of chemical in DW corresponding to an excess est lifetime cancer risk of 1 in 10,000

## Slide 9: How Do We Test?
Current Test Methods Generally Report 14 to 28 PFAS Depending on Laboratory
EPA Methods (527.1 and 533) are available for drinking water, MEDEP using modified isotope dilution methods except at public water supplies

## Slide 10: PFAS Primer – Simplified Groundwater Pathway CSM
Sources
Biosolids in the 1980s to early 2000s
Hilltop Fields
Thin Soils

## Slide 11: PFAS Primer – Simplified Groundwater Pathway CSM
Many Areas on Private Wells
Once in Bedrock Aquifer, Little Attenuation
NE/SW Fracture Control
Potential Surface Water Pathway

## Slide 12: Simplified Groundwater Pathway CSM - Receptors

## Slide 13: Simplified Groundwater Pathway CSM - Receptors
Other Factors:
River and Smaller Drainages
Public Water: Extent and Locations
Not Connected

## Slide 14
Chris Evans
Gordon.c.evans@maine.gov