| Bureau of Labor Standards / OSHA – References: | OSHA 1910.178 |
| --- | --- |
| Forklift, Electric or Propane (LNG) |  |
| Locations: | Automotive Shops Battery Charging Areas Loading Area |
| Inspector: | The person, appointed by the CTE, inspecting the forklift should know: Hazards Location of each facility Required training Proper procedures for inspecting. |
| Frequency of Inspections: | At a minimum Monthly Should be inspected prior to use by authorized driver. |
| Inspection: | See Attached Form |

Operator's Daily Checklist - Internal Combustion Engine Industrial Truck - Gas/LPG/Diesel Truck

Record of Fuel Added

| Date |  | Operator |  | Fuel |  |
| --- | --- | --- | --- | --- | --- |
| Truck# |  | Model# |  | Engine Oil |  |
| Department |  | Serial# |  | Radiator Coolant |  |
| Shift |  | Hour Meter |  | Hydraulic Oil |  |
| SAFETY AND OPERATIONAL CHECKS (PRIOR TO EACH SHIFT) Have a qualified mechanic correct all problems. |
| Engine Off Checks | OK | Maintenance |
| Leaks – Fuel, Hydraulic Oil, Engine Oil or Radiator Coolant |  |  |
| Tires – Condition and Pressure |  |  |
| Forks, Top Clip Retaining Pin and Heel – Check Condition |  |  |
| Load Backrest – Securely Attached |  |  |
| Hydraulic Hoses, Mast Chains, Cables and Stops – Check Visually |  |  |
| Overhead Guard – Attached |  |  |
| Finger Guards – Attached |  |  |
| Propane Tank (LP Gas Truck) – Rust Corrosion, Damage |  |  |
| Safety Warnings – Attached (Refer to Parts Manual for Location) |  |  |
| Battery – Check Water/Electrolyte Level and Charge |  |  |
| All Engine Belts – Check Visually |  |  |
| Hydraulic Fluid Level – Check Level |  |  |
| Engine Oil Level – Dipstick |  |  |
| Transmission Fluid Level – Dipstick |  |  |
| Engine Air Cleaner-Squeeze Rubber Dirt Trap or Check the Restriction Alarm (if equipped) |  |  |
| Fuel Sedimentor (Diesel) |  |  |
| Radiator Coolant – Check Level |  |  |
| Operator's Manual – In Container |  |  |
| Nameplate – Attached and Information Matches Model, Serial Number and Attachments |  |  |
| Seat Belt – Functioning Smoothly |  |  |
| Hood Latch – Adjusted and Securely Fastened |  |  |
| Brake Fluid – Check Level |  |  |
| Engine On Checks – Unusual Noises Must Be Investigated Immediately | OK | Maintenance |
| Accelerator or Direction Control Pedal – Functioning Smoothly |  |  |
| Service Brake – Functioning Smoothly |  |  |
| Parking Brake – Functioning Smoothly |  |  |
| Steering Operation – Functioning Smoothly |  |  |
| Drive Control – Forward/Reverse – Functioning Smoothly |  |  |
| Tilt Control – Forward and Back – Functioning Smoothly |  |  |
| Hoist and Lowering Control – Functioning Smoothly |  |  |
| Attachment Control – Operation |  |  |
| Horn and Lights – Functioning |  |  |
| Cab (if equipped) – Heater, Defroster, Wipers – Functioning |  |  |
| Gauges: Ammeter, Engine Oil Pressure, Hour Meter, Fuel Level, Temperature, Instrument Monitors – Functioning |  |  |

Operator's Daily Checklist - Electric Industrial Truck

Record of Fluid Added

| Date |  | Operator |  | Battery Water |  |
| --- | --- | --- | --- | --- | --- |
| Truck# |  | Model# |  | Hydraulic Oil |  |
| Department |  | Serial# |  |  |  |
| Shift |  | Drive Hour Meter Reading |  | Hoist Hour Meter Reading |  |

SAFETY AND OPERATIONAL CHECKS (PRIOR TO EACH SHIFT)

Have a qualified mechanic correct all problems

| Motor Off Checks | OK | Maintenance |
| --- | --- | --- |
| Leaks – Hydraulic Oil, Battery |  |  |
| Tires – Condition and Pressure |  |  |
| Forks, Top Clip Retaining Pin and Heel -- Condition |  |  |
| Load Backrest Extension – Attached |  |  |
| Hydraulic Hoses, Mast Chains, Cables & Stops – Check Visually |  |  |
| Finger Guards – Attached |  |  |
| Overhead Guard – Attached |  |  |
| Safety Warnings – Attached (Refer to Parts Manual for Location) |  |  |
| Battery – Water/Electrolyte Level and Charge |  |  |
| Hydraulic Fluid Level – Dipstick |  |  |
| Transmission Fluid Level – Dipstick |  |  |
| Operator's Manual in Container |  |  |
| Capacity Plate Attached – Information Matches Model, Serial Number and Attachments |  |  |
| Battery Restraint System – Adjust and Fasten |  |  |
| Operator Protection Sitdown Truck - Seat Belt – Functioning Smoothly Man-up Truck – Fall protection/Restraining means - Functioning |  |  |
| Brake Fluid – Check level |  |  |
| Motor On Checks (Unusual Noises Must Be Investigated Immediately) | OK | Maintenance |
| Accelerator Linkage – Functioning Smoothly |  |  |
| Parking Brake – Functioning Smoothly |  |  |
| Service Brake – Functioning Smoothly |  |  |
| Steering Operation – Functioning Smoothly |  |  |
| Drive Control – Forward/Reverse – Functioning Smoothly |  |  |
| Tilt Control – Forward and Back – Functioning Smoothly |  |  |
| Hoist and Lowering Control – Functioning Smoothly |  |  |
| Attachment Control – Operation |  |  |
| Horn – Functioning |  |  |
| Lights & Alarms (where present) – Functioning |  |  |
| Hour Meter – Functioning |  |  |
| Battery Discharge Indicator – Functioning |  |  |
| Instrument Monitors – Functioning |  |  |

ALL OPERATORS MUST BE TRAINED AND EVALUATED ON THE TYPES OF INDUSTRIAL TRUCKS AND ATTACHMENTS THEY WILL BE OPERATING.