Math-in-CTE Lesson Plan Template

| Lesson Title: Power tool | Lesson # 6 |
| --- | --- |
| Author(s): | Phone Number(s): | E-mail Address(es): |
| Ed Stout | 802-476-6237ext2016 | estoubvt@u61.net |
| Brenda Waterhouse | 802-476-4811 ext1190 | bwateshs@u61.net |
| Occupational Area: Electrical Technology |
| CTE Concept(s): Power tool |
| Math Concepts: Percents to Decimals; Multiplication & Division; Using & Solving Formulas |
| Lesson Objective: | Students will develop an understanding of power cord safety, how to calculate voltage drop and determining wire size. |
| Supplies Needed: | Various power tools with name plates, Various extension cords, Circular Mil Table; Voltage Powerpoint ; voltage pre-test, voltage practice, voltage post-test |

| The "7 Elements" | Teacher Notes (and answer key) |
| --- | --- |
| Introduce the CTE lesson. Extension cord safety and use for power tools How are extension cords rated for capacity How are cords sized (Gauge Size) What is voltage drop How does voltage drop affect power tools | OSHA requirement of no extension cords plugged together. Molded plug cords cannot have attached end caps. Extension cords can be made to custom length and gauge with attached end caps using UL listed materials. Electric motors run at 10% above intended operating temperature have motor life reduced by 50% Higher current draw reduces the life of electric power tools and increases the chance of fire because of extension cords operating too hot. |
| Assess students’ math awareness as it relates to the CTE lesson. Calculating Percentage What is 3% of line voltage? 120 vac and 240 vac Pre-test on % and manipulating formulas | Find out if students are unable to calculate % Find out if students are unable to manipulate formulas Voltage Pre test 32 amps $495.00 voltage =power / current current = voltage / resistance voltage = power / current |
| Work through the math example embedded in the CTE lesson. Introduce voltage drop formula Circular Mil Area K constant Practice problems | Use power point Explain: constant, Circular Mil Area, One mil=.001” I=current flow L=length of conductor Use K of 12 for Copper conductor 12 ohms of resistance for copper .001” thick, 1 foot long at 86ºF Constant number changes with change of material. Aluminum has different conductivity from copper |
| 4. Work through related, contextual math-in-CTE examples. Voltage drop value and % of source voltage Current draw values for different power tools Sizing wire for various current loads Using formulas, reading charts, calculations Develop understanding of American Wire Gauge (AWG) | Safety lesson of sizing conductors of extension cords for various power tool Math lesson in the process of sizing conductors |
| 5. Work through traditional math examples. Explanation of Voltage drop formula Demonstration of using Voltage drop Formula Practice problems | power point |
| 6.Students demonstrate their understanding. Practice problems work sheet | Several examples of construction site fixed and portable power equipment Table saw; Compound Miter saw; Lighting; Hammer drill; etc. Voltage Practice work sheet C 2. A 3. D 4. B |
| 7. Formal assessment. Post test on voltage drop,%, choosing wire gauge size | Voltage drop post test answer D 2. C 3.A 4. C |

NOTES: