Automotive Technology Standards and Competencies

Automobile/Automotive Mechanics Technology/Technician (47.0604)

Industry Organization Standard: National Automobile Technicians Education Foundation (NATEF) Maintenance and Light Repair (2012)

Framework, Duties and Tasks:

- Engine Repair - General

  - Research applicable vehicle and service information, vehicle service history, service precautions, and technical service bulletins.

  - Verify operation of the instrument panel engine warning indicators.

  - Inspect engine assembly for fuel, oil, coolant, and other leaks; determine necessary action.

  - Install engine covers using gaskets, seals, and sealers as required.

  - Remove and replace timing belt; verify correct camshaft timing.

  - Perform common fastener and thread repair, to include: remove broken bolt,    restore internal and external threads, and repair internal threads with thread insert.

  - Identify hybrid vehicle internal combustion engine service precautions.

- Engine Repair – Cylinder Head and Valve Train

  - Adjust valves (mechanical or hydraulic lifters).

- Engine Repair – Lubrication and Cooling Systems

  - Perform cooling system pressure and dye tests to identify leaks; check coolant condition and level; inspect and test radiator, pressure cap, coolant recovery tank, and heater core and galley plugs; determine necessary action.

  - Inspect, replace, and adjust drive belts, tensioners, and pulleys; check pulley and belt alignment.

  - Remove, inspect, and replace thermostat and gasket/seal.

  - Inspect and test coolant; drain and recover coolant; flush and refill cooling system with recommended coolant; bleed air as required.

  - Perform engine oil and filter change.

- Automatic Transmission and Transaxle – General

  - Research applicable vehicle and service information, fluid type, vehicle service history, service precautions, and technical service bulletins.

  - Check fluid level in a transmission or a transaxle equipped with a dip-stick.

  - Check fluid level in a transmission or a transaxle not equipped with a dip-stick.

  - Check transmission fluid condition; check for leaks.

- Automatic Transmission and Transaxle – In-Vehicle Transmission/Transaxle

- Inspect, adjust, and replace external manual valve shift linkage, transmission range sensor/switch, and park/neutral position switch.

- Inspect for leakage at external seals, gaskets, and bushings.

- Inspect replace and align power train mounts.

- Drain and replace fluid and filter(s).

- Automatic Transmission and Transaxle – Off-Vehicle Transmission and Transaxle

  - Describe the operational characteristics of a continuously variable transmission (CVT).

  - Describe the operational characteristics of a hybrid vehicle drive train.

- Manual Drive Train and Axles – General

  - Research applicable vehicle and service information, fluid type, vehicle service history, service precautions, and technical service bulletins.

  - Drain and refill manual transmission/transaxle and final drive unit.

  - Check fluid condition; check for leaks.

- Manual Drive Train and Axles – Clutch

  - Check and adjust clutch master cylinder fluid level.

  - Check for system leaks.

- Manual Drive Train and Axles – Transmission/Transaxle

  - Describe the operational characteristics of an electronically-controlled manual transmission/transaxle.

- Manual Drive Train and Axles – Drive Shaft, Half Shafts, Universal and Constant-Velocity Joints

  - Inspect, remove, and replace front wheel drive (FWD) bearings, hubs, and seals.

  - Inspect, service, and replace shafts, yokes, boots, and universal/CV joints.

- Manual Drive Train and Axles – Differential Case Assembly

  - Clean and inspect differential housing; check for leaks; inspect housing vent.

  - Check and adjust differential housing fluid level.

  - Drain and refill differential housing.

  - Drive Axles

    - Inspect and replace drive axle wheel studs.

- Manual Drive Train and Axles – Four-wheel Drive/All-wheel Drive

  - Inspect front-wheel bearings and locking hubs.

  - Check for leaks at drive assembly seals; check vents; check lube level.

- Suspension and Steering Systems – General

  - Research applicable vehicle and service information, vehicle service history, service precautions, and technical service bulletins.

  - Disable and enable supplemental restraint system (SRS).

- Suspension and Steering – Related Suspension and Steering Service

  - Inspect rack and pinion steering gear inner tie rod ends (sockets) and bellows boots.

  - Determine proper power steering fluid type; inspect fluid level and condition.

  - Flush, fill, and bleed power steering system.

  - Inspect for power steering fluid leakage; determine necessary action.

  - Remove, inspect, replace, and adjust power steering pump drive belt.

  - Inspect and replace power steering hoses and fittings.

  - Inspect pitman arm, relay (centerlink/intermediate) rod, idler arm and mountings, and steering linkage damper.

  - Inspect tie rod ends (sockets), tie rod sleeves, and clamps.

  - Inspect upper and lower control arms, bushings, and shafts.

  - Inspect and replace rebound and jounce bumpers.

  - Inspect track bar, strut rods/radius arms, and related mounts and bushings.

  - Inspect upper and lower ball joints (with or without wear indicators).

  - Inspect suspension system coil springs and spring insulators (silencers).

  - Inspect suspension system torsion bars and mounts.

  - Inspect and replace front stabilizer bar (sway bar) bushings, brackets, and links.

  - Inspect strut cartridge or assembly.

  - Inspect front strut bearing and mount.

  - Inspect rear suspension system lateral links/arms (track bars), control (trailing) arms.

  - Inspect rear suspension system leaf spring(s), spring insulators (silencers), shackles, brackets, bushings, center pins/bolts, and mounts.

  - Inspect, remove, and replace shock absorbers; inspect mounts and bushings.

  - Inspect electric power-assisted steering.

  - Identify hybrid vehicle power steering system electrical circuits and safety precautions.

  - Describe the function of the power steering pressure switch.

- Suspension and Steering – Wheel Alignment

  - Perform prealignment inspection and measure vehicle ride height; determine necessary action.

- Suspension and Steering – Wheels and Tires

  - Inspect tire condition; identify tire wear patterns; check for correct size and application (load and speed ratings) and adjust air pressure; determine necessary action.

  - Rotate tires according to manufacturer’s recommendations.

  - Dismount, inspect, and remount tire on wheel; balance wheel and tire assembly (static and dynamic).

  - Dismount, inspect, and remount tire on wheel equipped with tire pressure monitoring system sensor.

  - Inspect tire and wheel assembly for air loss; perform necessary action.

  - Repair tire using internal patch.

  - Identify and test tire pressure monitoring systems (indirect and direct) for operation; verify operation of instrument panel lamps.

  - Demonstrate knowledge of steps required to remove and replace sensors in a tire pressure monitoring system.

- Brakes – General

  - Research applicable vehicle and service information, vehicle service history, service precautions, and technical service bulletins.

  - Describe procedure for performing a road test to check brake system operation, including an anti-lock brake system (ABS).

  - Install wheel and torque lug nuts.

- Brakes – Hydraulic System

  - Measure brake pedal height, travel, and free play (as applicable); determine necessary action.

  - Check master cylinder for external leaks and proper operation.

  - Inspect brake lines, flexible hoses, and fittings for leaks, dents, kinks, rust, cracks, bulging, wear,  loose fittings and supports; determine necessary action.

  - Select, handle, store, and fill brake fluids to proper level.

  - Identify components of brake warning light system.

  - Bleed and/or flush brake system.

  - Test brake fluid for contamination.

- Brakes – Drum Brakes

  - Remove, clean, inspect, and measure brake drum diameter; determine necessary action.

  - Refinish brake drum and measure final drum diameter; compare with specifications.

  - Remove, clean, and inspect brake shoes, springs, pins, clips, levers, adjusters/self-adjusters, other related brake hardware, and backing support plates; lubricate and reassemble.

  - Inspect wheel cylinders for leaks and proper operation; remove and replace as needed.

  - Pre-adjust brake shoes and parking brake; install brake drums or drum/hub assemblies and wheel bearings; make final checks and adjustments.

- Brakes – Disc Brakes

  - Remove and clean caliper assembly; inspect for leaks and damage/wear to caliper housing; determine necessary action.

  - Clean and inspect caliper mounting and slides/pins for proper operation, wear, and damage; determine necessary action.

  - Remove, inspect, and replace pads and retaining hardware; determine necessary action.

  - Lubricate and reinstall caliper, pads, and related hardware; seat pads and inspect for leaks.

  - Clean and inspect rotor, measure rotor thickness, thickness variation, and lateral runout; determine necessary action.

  - Remove and reinstall rotor.

  - Refinish rotor on vehicle; measure final rotor thickness and compare with specifications.

  - Refinish rotor off vehicle; measure final rotor thickness and compare with specifications.

  - Retract and re-adjust caliper piston on an integral parking brake system.

  - Check brake pad wear indicator; determine necessary action.

  - Describe importance of operating vehicle to burnish/break-in replacement brake pads according to manufacturer’s recommendations.

- Brakes – Power-Assist Units

  - Check brake pedal travel with, and without, engine running to verify proper power booster operation.

  - Check vacuum supply (manifold or auxiliary pump) to vacuum-type power booster.

- Brakes – Miscellaneous (Wheel Bearings, Parking Brakes, Electrical, Etc.)

  - Remove, clean, inspect, repack, and install wheel bearings; replace seals; install hub and adjust bearings.

  - Check parking brake cables and components for wear, binding, and corrosion; clean, lubricate, adjust or replace as needed.

  - Check parking brake operation and parking brake indicator light system operation; determine necessary action.

  - Check operation of brake stop light system.

  - Replace wheel bearing and race.

  - Inspect and replace wheel studs.

- Brakes – Electronic Brakes, and Traction and Stability Control Systems

  - Identify traction control/vehicle stability control system components.

  - Describe the operation of a regenerative braking system.

- Electrical/Electronic Systems – General

  - Research applicable vehicle and service information, vehicle service history, service precautions, and technical service bulletins.

  - Demonstrate knowledge of electrical/electronic series, parallel, and series-parallel circuits using principles of electricity (Ohm’s Law).

  - Use wiring diagrams to trace electrical/electronic circuits.

  - Demonstrate proper use of a digital multimeter (DMM) when measuring source voltage, voltage drop (including grounds), current flow, and resistance.

  - Demonstrate knowledge of the causes and effects from shorts, grounds, opens, and resistance problems in electrical/electronic circuits.

  - Check operation of electrical circuits with a test light.

  - Check operation of electrical circuits with fused jumper wires.

  - Measure key-off battery drain (parasitic draw).

  - Inspect and test fusible links, circuit breakers, and fuses; determine necessary action.

  - Perform solder repair of electrical wiring.

  - Replace electrical connectors and terminal ends.

- Electrical/Electronic Systems – Battery Service

  - Perform battery state-of-charge test; determine necessary action.

  - Confirm proper battery capacity for vehicle application; perform battery capacity test; determine necessary action.

  - Maintain or restore electronic memory functions.

  - Inspect and clean battery; fill battery cells; check battery cables, connectors, clamps, and hold-downs.

  - Perform slow/fast battery charge according to manufacturer’s recommendations.

  - Jump-start vehicle using jumper cables and a booster battery or an auxiliary power supply.

  - Identify high-voltage circuits of electric or hybrid electric vehicle and related safety precautions.

  - Identify electronic modules, security systems, radios, and other accessories that require reinitialization or code entry after reconnecting vehicle battery.

  - Identify hybrid vehicle auxiliary (12v) battery service, repair, and test procedures.

- Electrical/Electronic Systems – Starting System

  - Perform starter current draw test; determine necessary action.

  - Perform starter circuit voltage drop tests; determine necessary action.

  - Inspect and test starter relays and solenoids; determine necessary action.

  - Remove and install starter in a vehicle.

  - Inspect and test switches, connectors, and wires of starter control circuits; determine necessary action.

- Electrical/Electronic Systems – Charging System

  - Perform charging system output test; determine necessary action.

  - Inspect, adjust, or replace generator (alternator) drive belts; check pulleys and tensioners for wear; check pulley and belt alignment.

  - Remove, inspect, and re-install generator (alternator).

  - Perform charging circuit voltage drop tests; determine necessary action.

- Electrical/Electronic Systems – Lighting Systems

  - Inspect interior and exterior lamps and sockets including headlights and auxiliary lights (fog lights/driving lights); replace as needed.

  - Aim headlights.

  - Identify system voltage and safety precautions associated with high-intensity discharge headlights.

- Electrical/Electronic Systems – Accessories

  - Disable and enable airbag system for vehicle service; verify indicator lamp operation.

  - Remove and reinstall door panel.

  - Describe the operation of keyless entry/remote-start systems.

  - Verify operation of instrument panel gauges and warning/indicator lights; reset maintenance indicators.

  - Verify windshield wiper and washer operation; replace wiper blades.

- Heating and Air Conditioning – General

  - Research applicable vehicle and service information, vehicle service history, service precautions, and technical service bulletins.

- Heating and Air Conditioning – Refrigeration System Components

  - Inspect and replace A/C compressor drive belts, pulleys, and tensioners; determine necessary action.

  - Identify hybrid vehicle A/C system electrical circuits and the service/safety precautions.

  - Inspect A/C condenser for airflow restrictions; determine necessary action.

- Heating and Air Conditioning – Heating, Ventilation, and Engine Cooling Systems

  - Inspect engine cooling and heater systems hoses; perform necessary action.

- Heating and Air Conditioning – Operating Systems and Related Controls

  - Inspect A/C-heater ducts, doors, hoses, cabin filters, and outlets; perform necessary action.

  - Identify the source of A/C system odors.

- Engine Performance – General

  - Research applicable vehicle and service information, vehicle service history, service precautions, and technical service bulletins.

  - Perform engine absolute (vacuum/boost) manifold pressure tests; determine necessary action.

  - Perform cylinder power balance test; determine necessary action.

  - Perform cylinder cranking and running compression tests; determine necessary action.

  - Perform cylinder leakage test; determine necessary action.

  - Verify engine operating temperature.

  - Remove and replace spark plugs; inspect secondary ignition components for wear and damage.

- Engine Performance – Computerized Controls

  - Retrieve and record diagnostic trouble codes, OBD monitor status, and freeze frame data; clear codes when applicable.

  - Describe the importance of operating all OBDII monitors for repair verification.

- Engine Performance – Fuel, Air Induction, and Exhaust Systems

  - Replace fuel filter(s).

  - Inspect, service, or replace air filters, filter housings, and intake duct work.

  - Inspect integrity of the exhaust manifold, exhaust pipes, muffler(s), catalytic converter(s), resonator(s), tail pipe(s), and heat shields; determine necessary action.

  - Inspect condition of exhaust system hangers, brackets, clamps, and heat shields; repair or replace as needed.

  - Check and refill diesel exhaust fluid (DEF).

- Engine Performance – Emissions Control Systems

  - Inspect, test, and service positive crankcase ventilation (PCV) filter/breather cap, valve, tubes, orifices, and hoses; perform necessary action.

- Required Supplemental Tasks

  - Shop and Personal Safety

    - Identify general shop safety rules and procedures.

    - Utilize safe procedures for handling of tools and equipment.

    - Identify and use proper placement of floor jacks and jack stands.

    - Identify and use proper procedures for safe lift operation.

    - Utilize proper ventilation procedures for working within the lab/shop area.

    - Identify marked safety areas.

    - Identify the location and the types of fire extinguishers and other fire safety equipment; demonstrate knowledge of the procedures for using fire extinguishers and other fire safety equipment.

    - Identify the location and use of eye wash stations.

    - Identify the location of the posted evacuation routes.

    - Comply with the required use of safety glasses, ear protection, gloves, and shoes during lab/shop activities.

    - Identify and wear appropriate clothing for lab/shop activities.

    - Secure hair and jewelry for lab/shop activities.

    - Demonstrate awareness of the safety aspects of supplemental restraint systems (SRS), electronic brake control systems, and hybrid vehicle high voltage circuits.

    - Demonstrate awareness of the safety aspects of high voltage circuits (such as high intensity discharge (HID) lamps, ignition systems, injection systems, etc.).

    - Locate and demonstrate knowledge of material safety data sheets (MSDS).

  - Tools and Equipment

    - Identify tools and their usage in automotive applications.

    - Identify standard and metric designation.

    - Demonstrate safe handling and use of appropriate tools.

    - Demonstrate proper cleaning, storage, and maintenance of tools and equipment.

    - Demonstrate proper use of precision measuring tools (i.e. micrometer, dial-indicator, dial-caliper).

  - Preparing Vehicle for Service

    - Identify information needed and the service requested on a repair order.

    - Identify purpose and demonstrate proper use of fender covers, mats.

    - Demonstrate use of the three C’s (concern, cause, and correction).

    - Review vehicle service history.

    - Complete work order to include customer information, vehicle identifying information, customer concern, related service history, cause, and correction.

  - Preparing Vehicle for Customer

    - Ensure vehicle is prepared to return to customer per school/company policy (floor mats, steering wheel cover, etc.).