Auto Body Standards and Competencies

Autobody/Collision and Repair Technology/Technician (47.0603)

Industry Standard(s): National Automobile Technicians Education Foundation (NATEF) Painting and Refinishing (2016)

Note: NATEF’s Painting and Refinishing tasks are the fourth of five sections in NATEF’s Collision Repair & Refinish task list.

Framework, Duties and Tasks:

- Safety Precautions

  - Identify and take necessary precautions with hazardous operations and materials according to federal, state, and local regulations.

  - Identify safety and personal health hazards according to OSHA guidelines and the “Right to Know Law”.

  - Inspect spray environment and equipment to ensure compliance with federal, state and local regulations, and for safety and cleanliness hazards.

  - Select and use a NIOSH approved air purifying respirator.  Inspect condition and ensure fit and operation.  Perform proper maintenance in accordance with OSHA Regulation 1910.134 and applicable state and local regulation.

  - Select and use a NIOSH approved supplied air (Fresh Air Make-up) respirator system.  Perform proper maintenance in accordance with OSHA Regulation 1910.134 and applicable state and local regulation.

  - Select and use the proper personal safety equipment for surface preparation, spray gun and related equipment operation, paint mixing, matching and application, paint defects, and detailing (gloves, suits, hoods, eye and ear protection, etc.).

- Surface Preparation

- Inspect, remove, store, and replace exterior trim and components necessary for proper surface preparation.

- Soap and water wash entire vehicle; use appropriate cleaner to remove contaminants.

- Inspect and identify substrate, type of finish, surface condition, and film thickness; develop and document a plan for refinishing using a total product system.

- Strip paint to bare substrate (paint removal).

- Dry or wet sand areas to be refinished.

- Featheredge damaged areas to be refinished.

- Apply suitable metal treatment or primer in accordance with total product systems.

- Mask and protect other areas that will not be refinished.

- Mix primer, primer-surfacer or primer-sealer.

- Identify a complimentary color or shade of undercoat to improve coverage.

- Apply primer onto surface of repaired area.

- Apply two-component finishing filler to minor surface imperfections.

- Dry or wet sand area to which primer-surfacer has been applied.

- Dry sand area to which two-component finishing filler has been applied.

- Remove dust from area to be refinished, including cracks or moldings of adjacent areas.

- Clean area to be refinished using a final cleaning solution.

- Remove, with a tack rag, any dust or lint particles from the area to be refinished.

- Apply suitable sealer to the area being refinished.

- Scuff sand to remove nibs or imperfections from a sealer.

- Apply stone chip resistant coating.

- Restore corrosion-resistant coatings, caulking, and seam sealers to repaired areas.

- Prepare adjacent panels for blending.

- Identify the types of rigid, semi-rigid or flexible plastic parts to be refinished; determine the materials, preparation, and refinishing procedures.

- Identify aluminum parts to be refinished; determine the materials, preparation, and refinishing procedures.

- Spray Gun and Related Equipment Operation

- Inspect, clean, and determine condition of spray guns and related equipment (air hoses, regulators, air lines, air source, and spray environment).

- Select spray gun setup (fluid needle, nozzle, and cap) for product being applied.

- Test and adjust spray gun using fluid, air and pattern control valves.

- Demonstrate an understanding of the operation of pressure spray equipment.

- Paint Mixing, Matching, and Applying

- Identify type and color code by manufacturer’s vehicle information label.

- Shake, stir, reduce, catalyze/activate, and strain refinish materials.

- Apply finish using appropriate spray techniques (gun arc, gun angle, gun distance, gun speed, and spray pattern overlap) for the finish being applied.

- Apply selected product on test and let-down panel; check for color match.

- Apply single stage topcoat.

- Apply basecoat/clearcoat for panel blending or panel refinishing.

- Apply basecoat/clearcoat for overall refinishing.

- Remove nibs or imperfections from basecoat.

- Refinish rigid or semi-rigid, and plastic parts.

- Refinish flexible plastic parts.

- Apply multi-stage coats for panel blending or overall refinishing.

- Identify and mix paint using a formula.

- Identify poor hiding colors; determine necessary action.

- Tint color using formula to achieve a blendable match.

- Identify alternative color formula to achieve a blendable match.

- Identify the materials equipment, and preparation differences between solvent and waterborne technologies.

- Paint Defects – Causes and Cures

- Identify blistering (raising of the paint surface, air entrapment); determine the cause(s) and correct the condition.

- Identify blushing (milky or hazy formation); determine the cause(s) and correct the condition.

- Identify a dry spray appearance in the paint surface; determine the cause(s) and correct the condition.

- Identify the presence of fish-eyes (crater-like openings) in the finish; determine the cause(s) and correct the condition.

- Identify lifting; determine the cause(s) and correct the condition.

- Identify clouding (mottling and streaking in metallic finishes); determine the cause(s) and correct the condition.

- Identify orange peel; determine the cause(s) and correct the condition.

- Identify overspray; determine the cause(s) and correct the condition.

- Identify solvent popping in freshly painted surface; determine the cause(s) and correct the condition.

- Identify sags and runs in paint surface; determine the cause(s) and correct the condition.

- Identify sanding marks or sandscratch swelling; determine the cause(s) and correct the condition.

- Identify contour mapping/edge mapping while finish is drying; determine the cause(s) and correct the condition.

- Identify color difference (off-shade); determine the cause(s) and correct the condition.

- Identify tape tracking; determine the cause(s) and correct the condition.

- Identify low gloss condition; determine the cause(s) and correct the condition.

- Identify poor adhesion; determine the cause(s) and correct the condition.

- Identify paint cracking (shrinking, splitting, crowsfeet or line-checking, micro-checking, etc.); determine the cause(s) and correct the condition.

- Identify corrosion; determine the cause(s) and correct the condition.

- Identify dirt or dust in the paint surface; determine the cause(s) and correct the condition.

- Identify water spotting; determine the cause(s) and correct the condition.

- Identify finish damage caused by bird droppings, tree sap, and other natural causes; correct the condition.

- Identify finish damage caused by airborne contaminants (acids, soot, rail dust, and other industrial-related causes); correct the condition.

- Identify die-back conditions (dulling of the paint film showing haziness); determine the cause(s) and correct the condition.

- Identify chalking (oxidation); determine the cause(s) and correct the condition.

- Identify bleed-through (staining); determine the cause(s) and correct the condition.

- Identify pin-holing; determine the cause(s) and correct the condition.

- Identify buffing-related imperfections (swirl marks, wheel burns); correct the condition.

- Identify pigment flotation (color change through film build); determine the cause(s) and correct the condition.

- Final Detail

- Apply decals, transfers, tapes, woodgrains, pinstripes (painted and taped), etc.

- Buff and polish finish to remove defects as required.

- Clean interior, exterior, and glass.

- Clean body openings (door jambs and edges, etc.).

- Remove overspray.

- Perform vehicle clean-up; complete quality control using a checklist.