Traffic Control Safety Checklist/Worksheet

Location:	 Date:	 Incident #:

Incident Commander:	 Safety Officer:

Vehicles on Scene:

Type of Incident:

Estimated Time On Scene:	 Less than 20 minutes 	 20 – 60 minutes	 More than 60 Minutes

Time of Day:	 Type of Roadway:	 Posted Speed Limit:

Weather Conditions:	 Light Conditions:

Traffic Conditions:	 Low 	 Moderate	 Heavy

Initial Traffic Control (Less than 60 minutes)	( Completed

Work area evaluated for hazards

Emergency vehicle positioned properly

Safety vests WORN

Advanced warning sign (1) placed (100’ – 1000’)

Traffic cones placed for taper (max of 20’ intervals) (100’ length)

Traffic cones placed along work area (max of 40’ intervals)

Emergency warning lights reduced

Law enforcement notified

Staging area established

Incident terminated - cones/signs removed

Set-Up (Initial)  Equipment Needed: Traffic cones (12), Emergency scene sign (1), Class 2 safety vest (2), Road flares (10)

Advanced Warning Area:	Distance		# of Signs

Transition Area (taper):	Distance		# of Cones

Work Area:	Distance		# of Cones

Temporary Traffic Control (More than 60 minutes)  	( Completed

Work area evaluated for hazards

Emergency vehicle positioned properly

Safety vests WORN

Advanced warning signs (2) placed (100’ - 1500’)

Transition area (taper) established (Cones – max of 20’ intervals) (max 100’ length)

Buffer space established

Work area established

Termination area established (Downstream taper) (max of 100’ per lane)

Flaggers with equipment positioned properly

Emergency air siren cans issued

Portable radios issued

Emergency warning lights reduced

Law enforcement traffic control points established

Local department of transportation on scene with advanced warning signs in place

Staging area established

Incident terminated - cones/signs removed

Set-Up (Temp.) Equipment Needed: Traffic cones (25-50), Emergency scene sign (2), Flagger signs (2), Stop/slow 
		   paddles (2), Emergency air siren cans (3), Portable radios (3), Class 2 safety vest (4), Road flares (1 case)

Advanced Warning Area:	Distance		  # of Signs  	  # of Flaggers

Transition Area (taper):	Distance		  # of Cones

Buffer Area:	Distance		  # of Cones

Work Area:	Distance		  # of Cones

Termination Area:	Distance		  # of Cones

Drawing

Miscellaneous Information

- One advanced warning sign – Urban (Low speed) – 100’, Urban (High speed) – 350’, Rural – 500’, 
	Expressways/Freeways – 1000’

- Second advanced warning sign – Urban (Low speed) – 100’, Urban (High speed) – 350’, Rural – 500’, 
	Expressways/Freeways – 1500’

- Buffer area – 30 MPH – 625’, 40 MPH – 825’, 50 MPH – 1000’, 60 MPH – 1300’, 70 MPH – 1450’

- One lane taper – 100’ max. – cone placement 10’ – 20’

- Downstream taper – 100’ per lane – cone placement – 10’ – 20’

- The equipment listed is the minimum required.  Additional safety vests may be required based on the 
	number of personnel on the scene

For additional information check with your State Department of Transportation and the Federal Highway Administration’s
Manual on Uniform Traffic Control Devices, Millennium Edition, http//mutcd.fhwa.dot.gov.

C10:213 (Rev. 4/03)