Table of Contents

Preparing the ExpressVote™	3

Starting the ExpressVote™	3

Voting with the ExpressVote™	4

Initiating the Voting Session………………………………………………..……………………………….…5

Selecting the Correct Ballot for the Voter………………………………..……………………………….…5

Voting a Card Using the Touch Screen	7

To Write-in a Candidate Using the Touch Screen	8

Voting a Card Using the Keypad	8

How to Vote Using the Sip-n-Puff	9

How to Vote Using the Rocker Paddle	10

Verifying a Marked Card	10

To Verify the Card	10

End of Voting Shut Down Procedures	11

Storing the ExpressVote™	11

Please contact Hardware Support with any questions at 1-877-ESS-VOTE Option 4, Option 1, or email hardware@essvote.com

REFERENCE: This guide is used as a quick start method for using the ExpressVote.

Additional details about the use of this machine can be found in the Standard Operation Guide.  By login on to your portal at http://www.essvote.com/portal

# Preparing the ExpressVote™

- Set up the white AVS voting table (provided with the prior AVS equipment) as directed in your Election Administrator’s Manual.

- Remove the ExpressVote™, power cord, and headphones from the carrying/storage case.

- Inspect the power cord for damage. If the cord is damaged, contact Elections Division or ES&S for a new cord.

- Place the ExpressVote™ face-down on the AVS table.  Plug the small circular end of the power cord (flat side up) into the port on the back of the ExpressVote.

- Deploy the kickstand and put the ExpressVote™ in the upright position.

- Plug the male end of the power cord into the wall outlet.

- Plug the headphones into the headphone port on the front of the unit.

- Ensure the keypad is plugged into the port in the Security Compartment on the left side of ExpressVote™ (this should already be done for you), and untether the keyboard from the Velcro fastening.

# Starting the ExpressVote™

Ensure the USB media device containing the current election definition is installed before the ExpressVote™ is powered on. The ExpressVote™ will not function if the USB media device is not installed.

- Unlock the Security Access Door on the left side of the machine.

- Insert the Election Definition memory stick inside the Security Access Door on the left side of the machine (if not already installed by the Clerk prior to Election Day).

- Set the power switch to On.

- Verify that the mode switch is set to Voter.

- On the Enter Election Code screen, enter the code provided by the Elections Division, and tap the Accept button.  Confirm that the system shows it is ready for voting, then select OK.

- Once the “To begin Voting, insert your card” screen appears, close and lock the access door, and give the wristlet to the Warden.

# Voting with the ExpressVote™

Election Officials need to understand how the voting process works using the ExpressVote™, so they may answer questions throughout the voting process. However, the Election Officials should not be involved in the vote selection process, unless requested by the voter to assist.

There are multiple ways for voters to interact and make choices on the card using the ExpressVote™.

- Using the touch screen, the Keypad, or the voter’s personal assistive device, along with the audio headphones.

# Initiating the Voting Session

- “To begin voting, insert your card” should be displayed on the screen.

- Insert an unmarked card into the input slot, with the cut corner oriented to the top right side (as indicated by the shape of the entry to the ballot slot).

# Selecting the Correct Ballot for the Voter

Once the voter inserts the ExpressVote™ ballot card, the Election Official will have to select the necessary precinct and/or ballot style.   The Election Official performs the following steps to search for a ballot style by precinct on the Precinct Search screen:

- Enter a search term, for example “Bangor”, or simply tap the Search button, to bring up a selection of precincts available for that voting place.

- Review the available precinct selections and choose the appropriate option for your election by tapping that option on the screen.

- After tapping the precinct button, a list of ballot style options will appear. Tap the appropriate option.

- After selecting the ballot style, the Ballot Confirmation screen will appear. Do one of the following:

•   Tap Activate after verifying that the precinct and ballot styles are correct, and proceed to Voting a Card Using the Touch Screen.

- Tap New Search to return to the Precinct Search screen if you need to see additional options.

# Voting a Card Using the Touch Screen

- The voter may use the buttons at the bottom of the screen to access display options and navigate the card (Previous, Zoom, Exit, Contrast, and Next).

  - The Zoom button will change the size of the display font between the normal font and a larger size font to meet the individual voter’s needs. In any instance where the contest extends off the screen, a More navigation bar will be displayed allowing the voter to scroll up and down to see the entire content of the contest.

  - The Exit button will return the voter’s unmarked card.

  - The Contrast button will change the display between the normal full color view and a high contrast black and white view (white text on a black background).

  - The Previous and Next buttons are used to proceed backward and forward between contests.

- Select a candidate or contest choice by touching the oval or anywhere on the line.

- The selection will be highlighted in yellow, and a check mark will appear next to the selection.

In a “Vote for ONE” contest, if the voter wishes to change the selection, the voter will simply touch on a new choice. The previous selection will be de-selected and the new selection will be highlighted with a check mark adjacent to it.

In a “multiple vote for” contest, once the voter has selected the maximum number of choices and attempts to select an additional choice, a message will be displayed indicating that the voter has overvoted. To change a selection, the voter must first de-select the previous choice and then make a new selection.

If the election is coded with an alert for undervotes, an undervote message is displayed if the voter fails to choose, or opts not to make a selection, in a contest. The voter may either return to the contest and make a selection, or continue to the next contest without making a selection.

# To Write-in a Candidate Using the Touch Screen

- On a contest screen, where applicable, select Write-In. Enter your choice for the write-in using the keyboard.

- Press Accept to accept the write-in and return to the previous screen. The write-in line will be highlighted in yellow, a check mark will appear next to your selection, and your write-in text will be displayed.

- When the voter has completed making the selections in each contest, the Verify Selections screen is displayed for review. Any undervoted contests will have an orange exclamation point to the left of the contest. If the voter wishes to re-visit a contest to change a selection, touch the contest on the review screen and that contest will be displayed. After making any changes, press the Next button and the voter will be returned to the Verify Selections screen.

- When the voter is done reviewing the selections, press the Next button to continue.

- If the voter is ready to mark the card, press the Print Card button. The card will be marked and returned to the voter.

- Remove the marked card. The “To begin voting, insert your card” screen will appear.

- Submit the card into the ballot box or tabulator for tabulation.

# Voting a Card Using the Keypad

#### Voters can use the keypad to maneuver through the ballot and make choices. Typically the keypad is used by voters with visual impairments and headphones should be used to hear the ballot instructions.

- Insert unmarked card into the ballot feed tray.

- The Election Official chooses the correct ballot style for the voter (as previously described).

- The ballot will be identified and the Voting Instructions will be read. The use of the keypad keys will be explained.

- Press the Right Arrow key to proceed to the first contest. The contest, the quantity available to vote for, and the number of choices available for selection, will be identified.

- Use the round Repeat key to have the last spoken phrase repeated.

- Use the Tempo key to adjust the speed at which the synthesized voice reads the text. Each time Tempo is pressed the current phrase will be re-started at the newly selected speed.

- Use the Volume key to adjust the synthesized speech to your personal comfort level.

- Use the diamond shaped Screen key to toggle the monitor screen on and off. The screen would typically be turned off for privacy, while voting the audio ballot.

- Press the Down Arrow key to scroll through the choices within a contest.

- Use the Select key to select a choice once it has been read.

- If you wish to change your selection in a “Vote for ONE” contest, simply scroll to your new choice and press the Select key. The new selection will override your previous selection.

|  | Voters may bring personal assistive devices for use at the polls that Maine does not supply to the municipalities. These instructions are provided for reference. |
| --- | --- |

# How to Vote Using the Sip-n-Puff

Sip-N-Puff refers to the interface device commonly used by a person with a disability, generally in a wheel chair, using his/her mouth on a straw to send inputs to the ExpressVote™. The voter sips or puffs on the straw to navigate the card and make selections.

The Sip-N-Puff device plugs into the accessibility port on the front panel of the ExpressVote™. Typically, the voter will supply the device.

Using only sips and puffs of air, the voter can negotiate all screens. When the voter arrives at any screen, they use a puff of air to choose to use that screen or suck in air (sip) to bypass the screen.

If they choose the screen, then the first selection on that screen will be highlighted. They then choose that selection by puffing into the straw. To continue to the next selection they will sip into the straw. This moves them to the next selection where they’ll either choose the selection (puff) or continue to the next selection (sip).

Now the voter sips to move to the bottom of the list and highlights the Next button. If the voter sips again, the highlight will move left along the navigation buttons at the bottom of the screen. If they continue to sip, the highlight will cycle back to the first selection option.

With the selection of the Next button, the voter will puff when the button is highlighted to select Next and move forward in the card.

The voter will continue in this manner to complete their card choices, then puff (select) the Print Card button when highlighted to complete the marking of the card.

# How to Vote Using the Rocker Paddle

Rocker Paddle refers to the interface device commonly used by a person with a disability using his/her hands or feet to make selections instead of pressing the touch screen. The voter uses the paddle to indicate YES or NO.

The Rocker Paddle device plugs into the accessibility port on the front panel of the ExpressVote™.

Using only yes/no, the voter can negotiate all screens. When the voter arrives at any screen, they choose YES to use that screen or NO to bypass the screen.

If they choose YES then the first selection on that screen will be highlighted. They then choose YES to make that selection or NO to move to the next selection.

For example, if there is a contest screen with two candidates the user selects YES when they arrive at the screen to indicate they want to vote in this race. (NO would skip the race). The first candidate will be highlighted in yellow. If they say YES then the first candidate will be selected and the highlight will move to the next candidate.

Now the voter selects NO to move to the bottom of the list and highlights the Next button. If the voter says NO again, the highlight will move left along the navigation buttons at the bottom of the screen. If they continue to choose NO, the highlight will cycle back to the first selection option.

# Verifying a Marked Card

The ExpressVote™ allows the voter to re-insert their marked card with printed vote selections into the input slot and verify their card choices. Note that no changes can be made from this verification step and the voter will only be able to view and hear the summary screen. If the voter wants to make changes, they will need to contact an election official to spoil the card (i.e., designate a spoiled ballot) and be given a blank card to begin the voting process over.

# To Verify the Card

- Insert the marked card into the input slot.

- A screen appears and instructions are read regarding how to verify the votes.

- Press Next or the Right Arrow to access the Verification Summary screen.

- Review the selections that are marked on the card.

- When done, press Next or the Right Arrow key.

- When instructed to do so, remove the card from the input slot.

- Submit the marked card to the ballot box or tabulator for tabulation.

# End of Voting Shut Down procedures

- Obtain the Access Door Key from the Warden.

- Unlock the access door and flip the power switch to the Off position.

- Keeping the keypad connected, close and lock the access door, and then remove the key.

# Storing the ExpressVote™

NOTE: Assure the ExpressVote™ is turned off by following the first step under End of Voting Shut Down Procedures.

- Unplug the headphones.

- Unplug the power cord from the wall outlet.

- Remove the power cord from the ExpressVote™.

- Place the ExpressVote™, with the keypad connected, into the black carrying case and zip it closed.  Place the power cord and headphones into the outside pouch of the carrying case.  Put the carrying case inside the plastic bag provided, and place the bagged carrying case into the delivery carton.

- Return the carton to the storage location and store according to the instructions provided on your User Agreement.

# Text boxes

ExpressVote™

Election Day Manual – Maine 2016

EVS 5.2.1.0

Version 1.4.1.0

Screen Off/ On

Audio Repeat

Audio Speed

Volume

Forward/Next

Scroll Up

Select

Back

Scroll Down

Opens voting instructions screen

Stops audio message