Table of Contents

I. Preparing the ExpressVote for Operation	3

Supplies and Equipment Checklist	3

II.    Preparing the ExpressVote™ for Use	4

Starting the ExpressVote™	5

Clearing the ExpressVote™	5

Loading the Election Definition (Poll Media)	7

Main Menu	8

Check Polling Place Information	9

Check Battery Status	9

Battery Status Screen Information	10

Calibrate the Touch Screen	11

System Maintenance Menu	12

Check the Date and Time	12

Testing the Election Definition	14

Testing the ExpressVote™	15

Vote a Ballot/Activator Card Using the Touch Screen	16

Write-in a Candidate Using the Touch Screen	16

Vote a Card Using the Keypad	17

Write-in a Candidate Using the Keypad	18

Vote Using an Assistive Technology Device	18

Mark the Ballot(s)	19

IV. End-of-Testing Procedures	20

Charging the Battery	20

Powering Down and Storing ExpressVote™	20

I. Preparing the ExpressVote™ for Operation

- Remove the ExpressVote™, power cord, and headphones from the carrying/storage case. (The access key should not be kept in the carrying case but in a separate, secure location).

- Check supplies against the list (below).

- Check for availability of all support contact information and manuals.

- Inspect power cord equipment for damage. If the cord is damaged, contact the Elections Division for a new cord.

- Use the alcohol wipes to clean the outside panels and screen of the ExpressVote™ unit.

- Wait till the unit is dry before proceeding to start-up and battery check.

- Operating Tip 1 Never use products with ammonia to clean the touch screen - this could eventually damage the screen.

# Supplies and Equipment Checklist

| USB Flash Drives - EQC Media, and Election Definition (Poll Media) |  |
| --- | --- |
| 1 Set of Headphones |  |
| 1 Keypad |  |
| 1 clean lint free cloth |  |
| Blank thermal ballot cards (“activators”) of the correct length for the election |  |
| 1 container of alcohol wipes |  |
| 1 set of ExpressVote™ keys |  |
| ExpressVote™ power cord (in two pieces: transformer and EV unit plug; power outlet plug) |  |
| Extension cord if required – Commercial Grade Orange or Yellow only (from the previous AVS kit) |  |
| Surge protector (from the previous AVS kit) |  |

****************

# II.    Preparing the ExpressVote™ for Use

During the preparation process you will:

- Power the unit up

- Clear the ExpressVote™ of previous election information

- Load the current election definition

- Access the unit’s Main Menu and System Maintenance Menu

- Check the Polling Place Information on the ExpressVote™

- Check battery status (Main Menu)

- Calibrate the ExpressVote™ touch screen (Main Menu)

- Check the unit’s date and time settings and make corrections if necessary (System Maintenance Menu)

- When navigating through the menus, keep in mind that with the exception of time/date, the options in the System Maintenance Menu are intended for the use of technicians.

# Starting the ExpressVote™

With the unit face-down on a table, plug the power cord into the power port on the back of the ExpressVote™ (flat side of the plug facing up) and then plug the AC power cord from the external power supply into a standard, grounded, three-prong 120-volt wall outlet.

- The power cord only plugs into the ExpressVote™ one way (flat side up). Do not attempt to force the power cord into the ExpressVote unit.

- Only plug the ExpressVote™ into a grounded, three-pronged electrical outlet. Plug only one ExpressVote™ into each outlet.

- Connect the keypad to the port in the Security Compartment on the left side of the ExpressVote™. The unit is delivered with the keypad attached. If otherwise, please contact the Elections Division.

- Plug the headphones into the headphone jack in the front of the unit (optional).

- Move the power switch to the “ON” position.  This switch is located in the Security Compartment on the left side of the ExpressVote™.

- Set the Mode Switch (also in the Security Compartment) to “Official” to access the ExpressVote Main Menu.

# Clearing the ExpressVote™

Before loading the election definition, all previous election information will need to be cleared from the ExpressVote™ using the Election Qualification Code (EQC) device (USB media). Clearing the ExpressVote™ assures the following:

  - The election log from the previous election is cleared.

  - The public count is reset to zero.

The EQC device also loads the Election Qualification Code for the ExpressVote™ as well as all codes that were set in ElectionWare.

- On the left side of the ExpressVote™, gently insert the Election Qualification Code (EQC) media into one of the empty USB ports.

- Always inspect the memory stick ports to ensure that they are clear.  Do not force the memory stick into the ExpressVote™ unit. Inserting a memory stick into blocked ports will result in damage that is not covered under warranty.

- Once the system recognizes the EQC memory stick, proceed to the next step.

- On the Enter Clear and Initialize screen keyboard, type the EQC code in the appropriate field.

- If the wrong code is entered, press “Clear” and re-enter. Do not press the red Cancel button.

- When Accept is selected, the Clear and Initialize screen appears:

- Select Clear and Initialize to proceed with the clearing and initializing process.

- Remove the EQC memory stick from the ExpressVote™ unit when the confirmation message appears.

# Loading the Election Definition (Poll Media)

- The Election Definition must be correctly programmed before it is inserted into ExpressVote™.

  - If not already open, open the Security Compartment on the left side of the ExpressVote™ with the security key.

  - Insert the Election Definition memory stick into any USB port.

- Always inspect the memory stick ports to ensure that they are clear.  Do not force the memory stick into the ExpressVote™ unit. Inserting a memory stick into blocked ports will result in damage that is not covered under warranty.

  - The Detecting Media message appears as the system identifies the file type.

  - Enter in the necessary Election Code and press Accept.

- A progress status bar appears as ExpressVote™ decrypts and validates the election definition.

  - Confirm that the system shows it is ready for voting, and then Select OK.

- The ExpressVote™ will only permit operation of voting functions while the Election Definition media is plugged in. Do not remove the Election Definition media while the system is powered on.

# Main Menu

When you start the ExpressVote™ you will have access to different starting screens and menu options depending on:

- Whether you have started up in Official Mode or Voter Mode, or

- Whether or not the election media is plugged in and the security codes entered.

Starting up in Official Mode with no election media plugged in will bring up the ExpressVote™ Main Menu Screen but with the Polling Place Information and Provisional Ballot options locked. If you start up in Voter Mode with no media present you will start on the Not Ready for Voting screen. Switch to Official Mode to continue with the Pre-Election Day procedure.

After inserting the Election Definition media and entering the security code, the screen returns to the Main Menu (see below). From here you can check polling place information, check battery status, and enter the System Maintenance Menu to check and correct the date, time, and time zone.

# Check Polling Place Information

- Touch the Polling Place Information button from the Main Menu (this will not be available until the election definition memory stick has been plugged in).

- Verify your polling place information.

- If there are any inaccuracies, contact Elections Division immediately.

# Check Battery Status

- To ensure optimal battery performance it is recommended that the ExpressVote™ be charged overnight within forty-eight hours of Election Day.

Battery status information can be accessed by touching the Battery Status button on the Main Menu or by checking the battery status LED located on the front of the ExpressVote™ unit.

1. The Battery Status Screen:

# Battery Status Screen Information

| Option | Description |
| --- | --- |
| Power Source | Shows the source of the power to the unit: either “Battery” (back-up battery) or “External” (a 110 volt AC electrical outlet.) |
| Battery Strength | Shows the strength of the battery. |
| Battery Charge | Shows the following charge levels of the battery: Low – indicates the battery pack voltage is below about 16.2V. The hardware will turn on the red battery light on the auxiliary panel (if the unit is turned on). Not Low – indicates the battery pack voltage is equal to or above about 16.2V. The hardware will turn on the green battery light on the auxiliary panel (if the machine is turned on). Not Fully Charged – indicates the battery pack voltage is below about 20.3V. Fully Charged – indicates the battery pack voltage is equal to or above about 20.3V. |
| EXIT | Returns to the System Maintenance Menu screen. Always available by default. |

2. The Battery Status LED:

The ExpressVote™ also incorporates a battery status LED on the front of the unit. The LED displays the status of the battery and indicates whether or not the unit is currently plugged into an AC power source.

The LED’s Battery Status Indicators

| Power Cord Status LED Indicator | Appears green if the ExpressVote™ unit is connected to an AC power source. Does not need to have the power switch in the ON position to appear green. When AC power is present, but the unit is off, the Power Supply Board can still charge the internal battery pack. |
| --- | --- |
| Battery Status LED Indicators | Shows the battery charge levels. When the unit is turned off, both LEDs are not lit to conserve battery charge. When the unit is turned on, either the green or red battery LED is lit, not both. |
| Battery Green Status LED | Appears green if the battery pack is fully charged. |
| Battery Red Status LED | Appears red if the battery pack is anything lower than 100% or the battery pack is not connected to the ExpressVote™ unit. |

# Calibrate the Touch Screen

- This is not a routine step. Calibrate the touch screen only if the screen appears unresponsive or inaccurate.

- From the ExpressVote™ Main Menu screen, select Calibrate Touch Screen.

- Read the provided instructions, and then select the Start button.

- Once the calibration screen appears, select the moving target as it moves from the center to the adjacent corners of the screen.

- Do not confuse touch screen calibration with scanner calibration (accessed from the System Maintenance menu). Scanner calibration should only be performed by an ES&S technician.

- Touch screen calibration is also accessible for 10 seconds during the boot-up process.

- After completing the test, a final screen will appear with a 30 second counter. Tap the screen before the timer runs out to accept the calibration. Or, allow the timer to expire to reject the calibration settings.

- Do one of the following once the calibration has been completed successfully.

  - Select Redo to restart the calibration process.

  - Select Exit to continue to the Main Menu screen.

# System Maintenance Menu

After checking the polling place information, battery status, and touchscreen calibration (if necessary), you will need to access the System Maintenance Menu on the lower right side of the Main Menu screen (see p.8).

- Touch the System Maintenance menu button.

- Enter the maintenance menu security code.

- The System Maintenance Menu should now appear (see below).

# Check the Date and Time

- From the System Maintenance Menu, select Set Time Zone/Date/Time. The Set Time Zone/Date/Time screen appears. Make changes to time zone, date, or time as necessary.

- From the Set Time Zone/Date/Time screen, select the appropriate time zone from the available list.

- The default setting for the unit is to automatically adjust for daylight saving time – make sure that box is checked!

- To set the date, select the radio button next to the Date and then select CLEAR.

- Enter the date in the MM-DD-YY format and select APPLY.

- To set the time, select the radio button next to TIME and select CLEAR.

- Enter the new time in the HH:MM AM format and select APPLY.

- Select EXIT when finished editing the date and time.

- The “–“ and “:” symbols must be entered in manually when entering a new date and time.

- ExpressVote™ accepts 24-hour and 12-hour (AM/PM) entries. Please use 12-hour time. If PM is left off, the entry defaults to AM

- The ExpressVote™ must be rebooted for the change to the date and time to take effect.

III.    Testing the Election Definition and the ExpressVote™ Voting Functions

During the testing procedure you will:

- Test the election definition manually or with the DS200 tabulator

- Test the ExpressVote™ voting and assistive functions

  - Vote using the touch screen and the keypad

  - Use headphones in combination with the touch screen and keypad to check audio function

  - Test the write-in function for both touchscreen and keypad

  - Verify that alerts for under or over voting are functioning

  - Verify the accuracy of the marked ballot

  - Verify scanner accuracy

# Test the Election Definition

DS200 users:

Testing the Election Definition is completed by printing a deck of cards with a specified pattern and then scanning these cards with the DS200 tabulator.

- Obtain the number of cards required for the test deck pattern as instructed by the Elections Division

- Record the test deck result prior to tabulation

- Vote the test deck in accordance with the pattern

- Compare the tabulated election result with the test deck’s pre-recorded result

Hand-count test:

A test deck will not be used. Follow the test procedure outlined through the remainder of this section (III) of the manual. Check the accuracy of the marked ballot(s) after printing. One or two printed ballots will be sufficient to verify the accuracy of the printer and scanner.

# Testing the ExpressVote™

Perform thorough testing to ensure everything is in working order before the election. The sooner the tests are performed, the sooner an issue that may arise can be resolved. Multiple unmarked cards will be needed to test the loaded election definition.

- Turn the Mode switch to Voter.

- “To begin voting, insert your card” should be displayed on the screen.

- Insert an unmarked card into the ballot feed tray.

- Test all buttons at the bottom of the screen to ensure operation (Previous, Zoom, Exit, Contrast, and Next).

  - The Zoom button will change the size of the display font between the normal font and a larger size font to meet the individual voter’s needs. In any instance where the contest extends off the screen, a More navigation bar will be displayed allowing the voter to scroll up and down to see the entire content of the contest.

  - The Exit button will return the voter’s unmarked card.

  - The Contrast button will change the display between the normal full color view and a high contrast black and white view (white text on a black background).

  - The Previous and Next buttons are used to proceed backward and forward between contests.

# Vote a Ballot/Activator Card Using the Touch Screen

- Select a candidate or contest choice by touching the oval or anywhere on the line.

- The selection will be highlighted in yellow, and a check mark will appear next to the selected candidate.

In a “Vote for ONE” contest, if the voter wishes to change their selection they will simply touch their new choice.  The previous selection will be de-selected and the new selection will be highlighted with a check mark adjacent to it.

In a “multiple vote for” contest, once the voter has selected the maximum number of choices and attempts to select an additional choice, a message will be displayed indicating that the voter has over voted. If the voter wishes to change a selection, they must first de-select a previous choice and then make a new selection.

# Write-in a Candidate Using the Touch Screen

- On a contest screen, where applicable, the voter will select Write-In, and enter in their selection using the on screen keyboard.

- Once the selection has been entered, the voter will press Accept to accept the write-in and return to the previous screen. The write-in line will be highlighted in yellow, with a check mark to the left of the selection and the write-in text will be displayed.

- If the election is coded with an alert for undervotes, an undervote message is displayed if the voter fails to (or chooses not to) make a selection in a contest. The voter may then either return to the contest and make a selection, or continue to the next contest without making a selection.

# Vote a Card Using the Keypad

The ExpressVote™ is delivered with the keypad attached by Velcro to the left side of the unit, below the Secure Compartment. The keypad jack is located above the USB port used for election media (it will be plugged in at the time of delivery).

#### Voters can use the keypad to maneuver through the ballot and make choices. Typically the keypad is used by the visually impaired and headphones should be used to hear ballot instructions.

- Insert unmarked card into the ballot feed tray.

- If multiple precincts or ballot styles are available, follow the instructions in the Election Day Manual to select a certain ballot style for testing.

- The ballot will be identified and basic Voting Instructions will be read. Pressing the Home key will take the voter to the Voting Instructions screen where the use of the keypad keys will be explained.

- Press the Right Arrow key to proceed to the first contest. The contest, the quantity available to vote for, and the number of choices available for selection, will be identified.

- Use the round Repeat key to have the last spoken phrase repeated.

- Use the Tempo key to adjust the speed at which the synthesized voice reads the text. Each time Tempo is pressed the current phrase will be re-started at the newly selected speed.

- Use the Volume key to adjust the synthesized speech to the preferred comfort level.

- Use the diamond shaped Screen key to toggle the monitor screen on and off. The screen would typically be turned off for privacy, while voting the audio ballot.

- Press the Down Arrow key to scroll through the choices within a contest. Use the Select key to select a choice once it has been read. If the voter wishes to change a selection in a “Vote for ONE” contest, simply scroll to the new choice and press the Select key. The new selection will override the previous selection.

# Write-in a Candidate Using the Keypad

| On the Contest screen, select Write-In. You can press the Left Arrow key on the keypad to close the write-in screen without entering a candidate and return to the contest screen. On the Write-In screen, using the keypad, use the Up and Down arrow keys to scroll through each letter or option being read. Once the necessary letter or option appears, press Select. Once the preferred candidate has been entered in, the voter will need to press the Right Arrow key to accept the write-in and return to the previous screen. The write in candidate will be spelled back to the voter by the automated voice. To continue on to the next contest, the voter will simply press the Right Arrow. |  |
| --- | --- |
| If the election is coded to “Alert Under-votes”, and the voter has forgotten to, or has chosen not to make a selection in a contest, an Under-vote Alert directs the voter to either return to the contest and make a selection, or continue to the next contest without making a selection. Once all of the races are voted, the Verify Selections screen allows the voter to scroll through all of the contests and verify their selections. If the voter is satisfied with their selections, press the Right Arrow key. If the voter is ready to have their ballot marked, they will need to press the Select key. The ballot will be marked and returned to the voter. |

# Vote Using an Assistive Technology Device

ExpressVote™ provides an interface for a personal assistive device that voters with physical disabilities or limited dexterity can use to mark contest choices. This device is often called an assistive technology (AT) device, which allows the voter to make selections in place of pressing buttons on either the touch screen or the audio-tactile keypad. If an assistive device is to be used with the ExpressVote™, attach it to the unit by using the assistive port on the front of the unit.

# Mark the Ballot(s)

- When selections have been made in all contests, the Verify Selections screen is displayed for the voter to review each contest.

- Any undervoted contests will have an orange exclamation point to the left of the contest. If the voter wishes to re-visit a contest to change a selection, they will simply touch the contest on the review screen and that contest will be displayed.

- After making any changes, the voter will need to select the Next button and they will be returned to the Voter Selection screen.

- When the voter is done reviewing their selections, they will need to press the Next button to continue.

- If the voter is ready to mark their card, they will select the Print Card button.

- Once the card is ejected, the “Insert Your Ballot” screen will appear.

- Re-insert at least one marked ballot to verify scanner function. For write-ins, the scanner will read that a write-in selection has been made but will not display the written selection.

- The ExpressVote™ will not commence a new voting session when a marked ballot is inserted.

# IV. End-of-Testing Procedures

# Charging the Battery

The ExpressVote™ may be charged outside of its storage case by simply having its AC power cord plugged into an active outlet.

- The power LEDs on the front panel of the ExpressVote™ indicate the battery power level when external power is not being applied.

- Plug the power cord into the rear of the ExpressVote™.

- Plug the alternate end into an AC outlet.

- Once the battery is charged, turn the Mode switch to Official.

- From the ExpressVote™ Main Menu, select Battery Status.

- Confirm that the battery strength is Good.

# Powering Down and Storing ExpressVote™

- Use the security key to open the Security Compartment located on the left side of the unit and set the power switch to Off.

- Lock the compartment door and remove the key.

- Ensure all of the other doors on the machine are locked.

- Place the ExpressVote™ with the keypad connected into the black carrying case, place the carrying case inside the plastic bag provided, and place the bagged carrying case into the delivery carton.

- Store in your secure location according to the instructions provided in your User Agreement.

# Text boxes

EVS 5.2.0.2

Version 1.4.1.0

ExpressVote™

Pre-Election Day Manual – Maine 2016

ES&S Support

Elections Division

ELECTIONS TOLL FREE:

1-888-VOTESME

(1-888-868-3763)

ELECTIONS DIVISION:

1-207-624-7650

HARDWARE SUPPORT:

Please contact ES&S Hardware Support with any hardware questions at 1-877-ESS-VOTE, then Option 4 and Option 1. Or, email at:

Hardware@essvote.com

REFERENCE:

This guide is used as quick start method for using the ExpressVote. Additional details about the use of this machine can be found in the Standard Operation Guide via the portal at:

http://www.essvote.com/portal

This function displays the polling place for the dataset that is loaded

Screen Off

Audio Repeat

Volume

Scroll Up

Select

Back

Scroll Down

Opens voting instructions screen

Stops audio message

Audio Speed

Forward/Next